## Slide 1: Chapter 5 Finite State Machine
Dr. Ahmed Abou-Auf

## Slide 2: Finite State Machines
It is a synchronous sequential circuits
  Contain irregular pattern for next-state logic
  Used mainly as a controller in a large system
Mealy vs. Moore output
  Moore machine: output is a function of state
  Mealy machine: output function of state and input

## Slide 3: State Diagram as a Design Tool
States
  Each state is presented by a circle or a “bubble”
Transition between states
  The machine transits from one state to another when input condition is met
  The transition between states is presented by an arrow with logical expression of the inputs that represents the condition
Output
  Moore output: inside the state
  Mealy output: next to the input condition

## Slide 4: Example—Simple Memory Controller
Inputs from FPGA/ASIC logic
  reset: async reset
  clk: controller and memory clock
  mem: indicates memory operation when asserted (logic 1)
  rw: 1 read operation, 0 write operation
  burst: read 4 locations when asserted (logic 1)
  1
Outputs
  Output enable: oe (read)
  Write enable: we (write)
  Mealy output: me_we (write)
FPGA
Memory Controller
Memory
reset
clk
burst
mem
rw
oe
we
Note: address bus and data bus are not part of the memory controller.

## Slide 5: Simple Memory Controller—State Diagram
Operations
  write, read, read burst
6-state FSM
  Idle, write, read1, read2, read3, read4
Inputs
  reset, clk, mem, rw, burst
Outputs
  Output enable: oe
  Write enable: we
  Mealy output: me_we

## Slide 6: VHDL Implementation of FSM
Implementation Steps
  Break the design into the same blocks of the basic FSM model
  Infer the state register block
  Code the next-state logic according to the state diagram
  Code output logic according to the state diagram

## Slide 7: Example—VHDL (4-segment)

## Slide 8: Example—VHDL (4-segment)

## Slide 9: Example—VHDL (4-segment)

## Slide 10: Example—VHDL (2-segment)

## Slide 11: Example—VHDL (1-segment)

## Slide 12: Testbench

## Slide 13: mem_ctrl Simulation

## Slide 14: Moore vs Mealy output
Both machines have similar “computation capability”
But?
  Mealy uses less states
  Mealy more prone to input glitches
E.g., edge detection circuit
  A circuit to detect the rising edge of a slow “strobe” input and generate a “short” (about 1-clock period) output pulse
clk |  |  |  |  |  |  |  |  | 
strobe |  |  |  |  |  |  |  |  | 
rise_edge |  |  |  |  |  |  |  |  | 
rising edge detection

## Slide 15: Moore vs Mealy
Moore FSM
Mealy FSM

## Slide 16: RTL Implementation of the Moore FSM

## Slide 17: RTL Implementation of the Moore FSM

## Slide 18: Mealy FSM Edge Detection

## Slide 19: RTL Implementation of the Mealy FSM

## Slide 20: FSM Edge detection testbench

## Slide 21: Edge detection testbench

## Slide 22: Edge Detector Simulation

## Slide 23: Design Practical Edge Detector
clk |  |  |  |  |  |  |  |  |  |  |  | 
strobe |  |  |  |  |  |  |  |  |  |  |  | 
strobe_n |  |  |  |  |  |  |  |  |  |  |  | 
strobe_d |  |  |  |  |  |  |  |  |  |  |  | 
strobe_d_n |  |  |  |  |  |  |  |  |  |  |  | 
rise_edge |  |  |  |  |  |  |  |  |  | strobe | and | strobe_d_n
falling_edge |  |  |  |  |  |  |  |  |  | strobe_n | and | strobe_d
both_edge |  |  |  |  |  |  |  |  |  | strobe | xor | strobe_d

## Slide 24: Practical Edge Detector—No FSM
d
q
d
q
strobe
strobe_d
strobe_dd
clock

## Slide 25: Simulation

## Slide 26: Mixing FSM and Datapath

## Slide 27: Mixing FSM and Datapath
FSM
Datapath

## Slide 28: GCD—RTL

## Slide 29: GCD—RTL

## Slide 30: Testbench

## Slide 31: Simulation

## Slide 32: State Encoding
State assignment:
  assigns binary representations to symbolic states
  Good assignment reduce the complexity of next-state/output logic
Typical assignment
  Binary, Gray, one-hot, almost one-hot

## Slide 33: Synthesis mem_ctrl: Altera Quartus II

## Slide 34: mem_ctrl—state encoding: FSM Viewer

## Slide 35: mem_ctrl—state encoding: RTL Viewer

## Slide 36: Technology Map Viewer

## Slide 37: Optimization Options in Synthesis Settings

## Slide 38: mem_ctrl: state encoding minimum bits

## Slide 39: VHDL Synthesis Directives
Synthesis Directives:
  VHDL attributes: enum_encoding
Explicit VHDL Assignment
Notes: Attributes (user-defined)
Formal Definition
A value, function, type, range, signal, or constant that may be associated with one or more named entities in a description.
Simplified Syntax
attribute attribute_name: type; -- attribute declaration
attribute attribute_name of item : item_class is expression; -- attribute specification

## Slide 40: Handling the unused state
Problem:
  State presentation is not all inclusive—many unused states
  If there is no proper handling of the unused state, the FSM can hang up forever.
Solution
  Collect the unused states in an “others =>” clause and return to idle state.
Subtlety
  The above solution is ok for the explicit state assignment as the unused states are know at the VHDL level
  This is not the case for the enumerated states as the unused states are only known after synthesis and the “others=>” will be ignored by VHDL. However, synthesis tools take it into consideration.

## Slide 41: Tri-state buffer
Output with “high-impedance”
  VHDL description
      y <= 'Z' when oe=‘0' else
      a_in;
‘Z’ is not a value in Boolean algebra
  Can’t be used as input to logical operations
    f <= 'Z' and a;
    y <= data_a when in_bus='Z' else
    data_b;
Major application
  Bi-directional I/O pins
  Tri-state bus

## Slide 42: Tristate Synthesis Issue
Synthesis Problem
    with sel select
    y <= 'Z' when "00",
    '1' when "01"|"11",
    '0' when others;
Solution—separate tristate buffer
    with sel select
    tmp <= '1' when "01"|"11",
    '0' when others;
    y <= 'Z' when sel="00" else
    tmp;

## Slide 43: Bi-directional i/o pins—single tristate buffer

## Slide 44: Bi-directional i/o pins—double tristate buffer