## Slide 1: Chapter 3 VHDL Basics
Dr. Ahmed Abou-Auf
Spring 2018

## Slide 2: VHDL Lexical Elements
Identifier is the name of an object
  Can only contain alphabetic letters, decimal digits and underscore, the last character cannot be an underscore, no two successive underscores
  The first character must be a letter
  Not a reserved word
  Valid examples:
    A10, next_state, NextState, mem_addr_enable
  Invalid examples:
    sig#3, _X10, 7segment, X10_, hi_ _there
Numbers:
  Integer: 0, 1234, 98E7:
  Real: 0.0, 1.23456 or 9.87E6
  Base (2 – 16): 2#101101#
Character
  ‘1’, ‘0’
Strings
  Text Strings: “Hello”
  Bit strings: “1101”, B”1001”, O”372”, X”FAA0”

## Slide 3: VHDL Objects
A named item that hold a value of specific data type
Four kinds of objects
  Signal
  Variable
  Constant
  File (cannot be synthesized)
Signal:
  Declared in the architecture body's declaration section. Ports in entity declaration are considered as signals
  Signal declaration:
    signal signal_name, signal_name, ... : data_type;
  Signal assignment:
    signal_name <= projected_waveform;
  Can be interpreted as wires or “wires with memory” (i.e., FFs, latches etc.)

## Slide 4: VHDL Objects—cont.
Variable:
  Declared inside a process or a function/procedure.
  Variable declaration:
    variable variable_name, variable_name, ... : data_type;
  Variabe assignment:
    variable_name := projected_waveform;
  No direct hardware counterpart
  Contains no “timing info” (immediate assignment)
Constant
  Constant declaration:
    constant const_name, ... : data_type := value_expression
  Used to enhance readability
  Example

## Slide 5: Data Types
Definition of data type
  A set of values that an object can assume.
  A set of operations that can be performed on objects of this data type.
Frequently used data types:
  Standard VHDL types
  IEEE1164_std_logic package
  IEEE numeric_std package
    signed and unsigned has flexible operators and functions than std_logic_vectors
  User-defined types

## Slide 6: Standard VHDL types
integer:
  range: -(2^31) to 2^31-1, two subtypes: natural, positive
  Operators: +, -, *, /, abs, mod, rem, **
Real:
  range: -(1.0E+38) to (1.0E+38)
  Operators: +, -, *, /, abs, **
Time
  Similar to integer but has units: fs, ps, ns, us, ms, sec, min, hr
Boolean:
  (false, true)
  Boolean expression Operators: and, or, not, xor, nand, nor, xnor
  Relational operators returns boolean: =, >, >=, <, <=,
Bit:
  ‘0’, ‘1’
  Operators: and, or, not, xor, nand, nor, xnor
  Cannot be mixed with boolean: ‘0’ and true

## Slide 7: IEEE std_logic_1164 package
New data type: std_logic, std_logic_vector
  Replaces bit and bit_vector
  std_logic:
    – 9 values: ('U', 'X', '0', '1', 'Z', 'W', 'L', 'H', '-')
    • '0', '1': forcing logic 0' and forcing logic 1
    • 'Z': high-impedance, as in a tri-state buffer.
    • 'L' , 'H': weak logic 0 and weak logic 1, as in wiredlogic
    • 'X', 'W': “unknown” and “weak unknown”
    • 'U': for uninitialized
    • '-': don't-care.
  std_logic_vector: an array of elements with std_logic data type
  E.g.,
    signal a: std_logic_vector(7 downto 0);
  Need to invoke package to use the data type:
    library ieee;
    use ieee.std_logic_1164.all;
  Overloaded Logical operators: and, or, not, xor, nand, nor, xnor

## Slide 8: The std_logic type
is a resolved version of std_ulogic, this means there is a method to resolve the conflicts when one signal has multiple drivers

## Slide 9: Overloaded operators for std_logic_1164 package

## Slide 10: IEEE numeric_std package
Difficult to synthesize arithmetic operators from integer operands
    signal a, b, sum: integer;
    . . .
    sum <= a + b;
  IEEE numeric_std package: define integer as a an array of elements of std_logic
  Two new data types: unsigned, signed
  The array interpreted as an unsigned or signed binary number
  E.g.,
    signal x, y: signed(15 downto 0);
  Need invoke package to use the data type
    library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;

## Slide 11: IEEE numeric_std package—functions

## Slide 12: IEEE numeric_std package—operators.

## Slide 13: VHDL Type Cast and Conversion Functions

## Slide 14: Example: Simple ALU

## Slide 15: IEEE numeric_std package—examples
    library ieee;
    use ieee.std_logic_1164.all;
    use ieee.numeric_std.all;
    signal s1, s2, s3, s4, s5, s6: std_logic_vector(3 downto 0);
    signal u1, u2, u3, u4, u6, u7: unsigned(3 downto 0);
    signal sg: signed(3 downto 0);
    – Ok
    u3 <= u2 + u1; --- ok, both operands unsigned
    u4 <= u2 + 1; --- ok, operands unsigned and natural
    –Wrong
    u5 <= sg; -- type mismatch
    u6 <= 5; -- type mismatch
    – Fix
    u5 <= unsigned(sg); -- type casting
    u6 <= to_unsigned(5,4); -- conversion function
    –Wrong
    u7 <= sg + u1; -- + undefined over the types
    – Fix
    u7 <= unsigned(sg) + u1; -- ok, but be careful
    –Wrong
    s3 <= u3; -- type mismatch
    s4 <= 5; -- type mismatch
    – Fix
    s3 <= std_logic_vector(u3); -- type casting
    s4 <= std_logic_vector(to_unsigned(5,4));
    –Wrong
    s5 <= s2 + s1; + undefined over std_logic_vector
    s6 <= s2 + 1; + undefined
    – Fix
    s5 <= std_logic_vector(unsigned(s2) + unsigned(s1));
    s6 <= std_logic_vector(unsigned(s2) + 1);

## Slide 16: IEEE math_real—commonly used constants

## Slide 17: IEEE math_real—functions